## Slide 1: Group 4: Double-panel system
Apr. 4, 2022
Ben Masters, Senior in Acoustical Engineering
Eunseob Kim, Ph.D. Candidate in Mechanical Engineering
Jinghe Yu, M.S. Student in Mechanical Engineering
ME613: Advanced Engineering Acoustics
Homework 3a Presentation

## Slide 2: Analytical expression: Transfer matrix
Medium: Air
Two panels: homogeneous and limp
Panel 1
Airspace
Panel 2
Total (system)
p1
p2
u1z
u2z
z
x
where
Transfer matrix for a panel,
ρ0: Air density
c: Sound speed
ω: Frequency
k: wavenumber
[T]: Transfer function
ms: Mass per unit area
zm: in vacuo mechanical impedance
Zcn: Characteristic impedance referred to θ direction
p: Pressure
u: Particle velocity
R: Reflection coefficient
T: Transmission coefficient
θ: Angle of incidence
l: depth of airspace between panels
TL: Transmission loss
Nomenclature
x
z
R’
T’
T
θ
θ
θ
θ
θ
l
ms1
p1
p2
p3
p4
u1z
u2z
u3z
u4z
ms2
z=0
z=l
1
R
kz=kcosθ
z
x
p2
u2z
p3
u3z
l
Transfer matrix for airspace,
where

## Slide 3: Analytical expression: Transmission coefficient
=
…(1)
…(2)
If two panels are identical (zm1=zm2= zm =jωms),
Two identical Aluminum panels
ρ0 = 1.21 kg/m3
c = 340 m/s
ρAL = 2719 kg/m3
d = 1 mm
l = 100 mm
ms= ρALd = 2.710 kg/m3
Constant
x
z
1
R
T
θ
θ
θ
ms
p1
p4
u1z
u4z
z=0
z=100 mm
d
d
l
…(3)
where zmi = jωmsi and

## Slide 4: i) Normal incidence transmission loss
Transmission Loss goes to 0 at the Mass-Air-Mass Resonance.
Other Notable Characteristics:
  6 dB/oct ‘Mass Line’ below resonance
  18 dB/oct ‘Stiffness Line’ above resonance
ms1
ms1
ms
ms
Mass – Air – Mass
Two identical Aluminum panels
Mass line
(6 dB/oct)
Stiffness line (18 dB/oct)
Mass line
(6 dB/oct)
Stiffness line
(18 dB/oct)
ω0=1016 rad/s
Transmission Loss of Double Panel System

## Slide 5: ii) Comparison with approximation
The approximation line falls near the peaks of the double panel system.
Good approximation of TL above M-A-M resonance.
  Important to keep in mind the ‘peak and dip’ phenomena at high frequencies
Single panel case
z
Tsingle
θ
θ
θ
ms
z=0
1
R
x
d
Double Panel vs. Approximation

## Slide 6: iii) Single panel comparison
Single panel with a mass per unit area equal to the double panels.
  TL is equal before the M-A-M effect begins.
z
Tsingle
θ
θ
θ
ms,single
z=0
1
R
x
2d
z
Tdouble
θ
θ
θ
ms
z=0
1
R
x
d
d
l
z=l
Double-panel system
Single panel system
(no airspace)
Airspace
Double Panel vs. Single Panel

## Slide 7: iv) Effect of mass distribution of panel
Changing the mass distribution to 3:1, i.e. thickness of the two panels is changed to 1.5 mm and 0.5 mm.
Mass-air-mass resonance frequency increases
Transmission loss is not zero at this point.
ms
ms
ms1
ms2
d
d
1.5d
0.5d
Original system
New system
and

(Const.)
Assume
Transmission Loss and M-A-M Resonance
ω0=1016 rad/s
ω0=1173 rad/s

## Slide 8: v) Effect of ratio of l to λ on peaks and dips
The figure of transmission loss versus (airspace depth / wavelength) is plotted. The x-axis is in linear but not log scale:
  Dips appear when airspace depth equals to n/2 wavelength.
  Peaks appear between every two dips, that is when depth equals to (2n+1)/4 wavelength
The minima of dips are close to a mass line at very high frequency, but for the first several dips, they are not exactly on a mass line.

## Slide 9: vi) Effect of incidence angle (θ) on transmission loss
Increasing the angle of incidence
Normal, 30 degree, and 60 degree incidence cases are plotted.
It can be found the mass-air-mass resonance, dips and peaks all move to higher frequencies when incidence angle increases.
z
x
z
x
z
x
Normal incidence
θ=30°
θ=60°
θ=0°
θ
θ
pi
pi
pi

## Slide 10: Thank you for your attention!
Role
Eunseob Kim: Modeling and analytical solution
Ben Masters: MATLAB coding and solving i), ii), and iii)
Jinghe Yu: MATLAB coding and solving iv), v), and vi)